## Slide 1
Zahušťování digestátu z bioplynových stanic pomocí vakuového odpařování
Marek Vondra, m.vondra@vut.cz
Michal Touš
Vítězslav Máša
VUT v Brně, Fakulta strojního inženýrství, Ústav procesního inženýrství
TVIP, 19.10.2021, Hustopeče

## Slide 2: Motivation: number of biogas plants in Europe
Source: EBA, Annual Report 2020, January 2021

## Slide 3: Motivation: Biogas and biomethane potential
Source: EBA, Annual Report 2020, January 2021

## Slide 4: Motivation: BGP operation
nutrients (N,P,K)
+
90 % water
= natural
fertilizer
High storage & transport costs
Demand for volume reduction
180 Mt/y
in EU
(360 Mt/y
in 2030?)
Ineffective
use of
heat
50 %
wasted
250 kW
available

## Slide 5: Motivation: Benefits of the volume reduction
Reduction of the storage space
Fuel savings during digestate transportation
Fewer passes of agricultural machinery over farmland…
Emissions reduction (air, water, noise)
…and
through populated areas
Water
savings
Reduction of nitrogen
losses
Reduced
fees for
digestate
disposal
50-80 %
2-25 EUR/t
50-80 %
5000 m3/y

## Slide 6: Solution

## Slide 7: LIQUID DIGESTATE
SOLID FRACTION
DIGESTATE
Mechanical separation

## Slide 9: Waste heat production and utilization
Parameter | Value | Unit
pH | 7.5 – 8.1 | -
Dry matter | 2 – 12 | % wt.
N-NH4 | 3 000 – 5 000 | mg/l
COD | 30 – 60 | g/l
N-total | 3000 - 7000 | mg/l
P-total | 8 - 42 | g/kg DM
S-total | 2.9 – 14.7 | g/kg DM
Ca | 9 – 65.8 | g/kg DM
K | 28 - 95 | g/kg DM
Digestate
Parameter | Value | Unit
pH | 6.5 – 8.5 | -
TSS | 40 | mg/l
N-NH4 | 40 | mg/l
COD | 200 | mg/l
N-total | 60 | mg/l
P-total | 10 | mg/l
Separated water
Legal requirements for water discharge

## Slide 10: MSF evaporator prototype
Volume reduction up to 80%
Adjusted to LD: foaming, viscosity, high ammonia conc., H2SO4 formation
Up to 15 % of DM
Brno University of Technology
Ammonia
in distillate
3000 mg/l

## Slide 11: Stripping prototype
Chart: NH4-N removal during a stripping test
| 0 | 30 | 60 | 90 | 120 | 150 | 180
 | 0 | 72.0907 | 95.9566 | 99.0927 | 99.8817 | 98.9349 | 98.2643
 | 1267.5 | 353.75 | 51.25 | 11.5 | 1.5 | 13.5 | 22
Brno University of Technology
Air as a stripping gas
Random packing: ceramic saddles
Up to 95 % ammonia removal
Ammonia
below
40 mg/l

## Slide 12: Pilot plant in Dříteč (CZ)
Project starting in 2021
Designed capacity of 32 t/d
Thermal input 250 kW
Cooperation with industrial partners

## Slide 13: Alternative solution: Nitrification + Evaporation
Czech University of Life Sciences Prague
 |  | Distillate,A | Distillate,B | Input
N-NH4 | mg/l | 40 | 20 | 16
COD | mg/l | 13 | 16 | 11067
N-total | mg/l | 47.6 | 30.0 | 4540
P-total | mg/l | 0.52 | <0,10 | 79.33
S-total | mg/l | 0.58 | <0,5 | 425
Brno University of Technology

## Slide 14: Conclusions & Future work
Digestate thickening brings number of benefits
Proposed technology: evaporation + stripping
Sufficient quality of the separated water
From prototypes to full-scale pilot plant
Development of the thickening system
Reduction of investment costs and elektricity consumption
Pilot plant installation and testing

## Slide 15
Pilot plant for digestate reduction in biogas plants
BRNO UNIVERSITY OF TECHNOLOGY FACULTY OF MECHANICAL ENGINEERING Project reg. Nr.: FW03010481 (Technology Agency of the Czech Republic)
Acknowledgment
Strategic Partnership for Environmental Technologies and Energy Production
BRNO UNIVERSITY OF TECHNOLOGY FACULTY OF MECHANICAL ENGINEERING Project reg. Nr.: CZ.02.1.01/0.0/0.0/16_026/0008413

## Slide 16: Thank you.
Source: www.fli-energy.com
Marek Vondra
m.vondra@vut.cz