## Slide 1
Life cycle assessment of biowaste management: comparison of various alternatives in Prague
Aurore Guillaume
Supervisor: prof. Ing. Vladimír Kočí, Ph.D., MBA
ODPADOVÉ FÓRUM
21st, September 2022 - Hustopeče

## Slide 2: Introduction
Autopsy of mixed waste in Prague
EU objectives:
2023: container for biowaste
2030: reduce part of biodegradable waste going to landfill
 evaluate environmental impacts of current biowaste management situation in Prague
Biowaste: garden waste + kitchen waste
40%
25%
25%
6%
Non valuable

## Slide 3: Introduction
81% incineration
7% landfill
12% compost
0,03% anaerobic digestion
Part of mixed waste
Collected separately
 88.3 kg/capita/year biowaste in Prague

## Slide 4: Method
Biowaste collection (88.3 kg/capita/yr)
Transport
Incineration
Anaerobic digestion
Landfill
Compost
Avoided burden (energy + mineral fertilizer)
Life Cycle Assessment (LCA)

## Slide 5: Method
Source: Prague municipality, CENIA (Czech Environmental Agency), Pražské služby, literature
Impact assessment method: Environmental Footprint 3.0 (EF 3.0) and IPCC
Impact categories:
Climate change
Resource use (fossils)
Ecotoxicity to freshwater
Water use

## Slide 6: Results - Current situation in Prague
EF 3.0 normalized and weighted
Chart: 
| Climate Change - total | Ecotoxicity, freshwater - total | Resource use, fossils | Water use
Anaerobic digestion | 1.31e-08 | -3.52e-08 | -8.45e-08 | -1.2e-09
Compost | 3e-05 | -0.000104 | -4.95e-06 | -2.65e-06
Incineration | -0.000923 | -3.88e-05 | -0.000792 | 8.22e-05
Landfill | 0.000105 | 3.72e-06 | 7.07e-06 | 1.15e-07
Transport | 2.0473e-05 | 3.7183e-06 | 1.3368e-05 | 2.2914e-08

## Slide 7: Results – Different energy mix
EF 3.0 normalized and weighted
Electricity from power wind mix & Steam from biomass
Chart: 
| Climate Change | Ecotoxicity, freshwater | Resource use, fossils | Water use
Anaerobic Digestion | 1.2e-07 | -2.46e-08 | -3.49e-09 | -8.03e-10
Compost | 3e-05 | -0.000104 | -4.95e-06 | -2.65e-06
Incineration | 8.16e-05 | 3.85e-06 | 3.09e-05 | 6.91e-05
Landfill | 0.000105 | 3.72e-06 | 7.07e-06 | 1.15e-07
Transport | 2.0473e-05 | 3.7183e-06 | 1.3368e-05 | 2.2914e-08

## Slide 8: Results - Separate collection of biowaste
EF 3.0 normalized and weighted
BUT doesn’t include biogenic carbon in EF 3.0!
Chart: 
| Climate Change | Ecotoxicity, freshwater | Resource use, fossils | Water use
50/50 | 1.2295 | -2.4118 | 0.84685 | -1.1556
Community composting | 1.3142 | -5.1618 | 0.94878 | -1.2673
Anaerobic digestion | 1.0966 | 0.29779 | 0.71429 | -1.0432

## Slide 9: Results – Climate change
Chart: Climate change (kg CO2 eq)
| Anaerobic digestion | Compost | Incineration | Landfill | Transport
EF 3.0 | 0.000502 | 1.15 | -35.5 | 4.05 | 0.78748
IPCC | 0.00045 | 3.68 | 40.7 | 4.34 | 0.77247

## Slide 10: Results – Climate change - biowaste separation
Chart: Climate change
| 50/50 | Community composting | Anaerobic digestion
EF 3.0 | 1.2294 | 1.3142 | 1.0966
IPCC | -0.66061 | -0.40404 | -0.94606

## Slide 11: Discussion
Difficult to draw conclusion:
Biogenic carbon emissions?
Avoided burden: energy grid mix ?
Do we want to focus on avoided emissions or avoid direct emissions?
If we include biogenic emissions and we have a grid mix with more renewable energy, there are environmental benefits to separate biowaste
If we don’t consider biogenic emissions and with current energy sources, environmental benefits due to avoided burdens

## Slide 12: Conclusion
Climate change and resource use most important impact categories
Significant influence of energy grid mix
Different point of view: biogenic emissions ? Avoided burden ?
Locally dependent (improvement in technologies, transport, energy mix)
Future:
Production of biomethane from fermentation?
Anaerobic digestion more efficient and injection of steam to grid mix?

## Slide 13: References
Ekora. Oznámení záměru podle přílohy č. 3 zákona 100/2001 Sb. - Zpracování biologických odpadů v zařízení anaerobní digesce - Přibyšice; Prague, 2006.
Forbes, H.; Quested, T.; O'Connor, C. Generation, recovery and disposal of waste for the period 2020; Czech Statistical Office, 2021. https://www.czso.cz/documents/10180/143330119/28002021.pdf/41f799e9-3ffb-4702-a517-0c2dc1525144?version=1.3.
Petra Strouhalová. PILOTNÍ PROJEKT SBĚRU GASTROODPADŮ ŽIVOČIŠNÉHO A ROSTLINNÉHO PŮVODU Z DOMÁCNOSTÍ NA ÚZEMÍ HL.M. PRAHY; oddělení odpadů OCP MHMP,, 2021.
This project is supported by specific university research grant A2_FTOP_2022_009.
Thank you for your attention. Questions?

## Slide 14: Comparison between technologies
EF 3.0 normalized and weighted
Chart: 
| Anaerobic digestion | Compost | Incineration | Landfill
Climate Change | 9.48e-06 | 6.03e-05 | -0.000284 | 0.000424
Ecotoxicity, freshwater | -2.55e-05 | -0.00021 | -1.19e-05 | 1.5e-05
Resource use, fossils | -6.13e-05 | -9.95e-06 | -0.000244 | 2.84e-05
Water use | -8.7e-07 | -5.33e-06 | 2.53e-05 | 4.63e-07

## Slide 15: Results - Current situation in Prague
Chart: 
| Acidification | Climate Change - total | Ecotoxicity, freshwater - total | Eutrophication | Human toxicity - total | Ionising radiation, human health | Land Use | Ozone depletion | Particulate matter | Photochemical ozone formation, human health | Resource use, fossils | Resource use, mineral and metals | Water use
Anaerobic digestion | -5.89e-09 | 1.31e-08 | -3.52e-08 | 2.153e-09 | -3.412e-09 | -6.96e-09 | -2.07e-09 | -1.79e-11 | -1.01e-08 | 2.04e-09 | -8.45e-08 | -5.29e-09 | -1.2e-09
Compost | 1.42e-05 | 3e-05 | -0.000104 | 1.3165e-05 | -1.027e-06 | -1.26e-07 | -3.01e-07 | -6.46e-08 | 1.32e-05 | 4.16e-06 | -4.95e-06 | -2.19e-05 | -2.65e-06
Incineration | -2.77e-05 | -0.000923 | -3.88e-05 | -1.0046e-05 | -3.241e-05 | -2.75e-05 | -7.41e-06 | -1.42e-10 | -3.54e-05 | -1.55e-05 | -0.000792 | -4.29e-06 | 8.22e-05
Landfill | 1.83e-06 | 0.000105 | 3.72e-06 | 8.13e-06 | 2.744e-06 | 1.19e-07 | 3.85e-08 | 6.15e-13 | 2.36e-06 | 3.33e-06 | 7.07e-06 | 3.2e-08 | 1.15e-07
Transport | 5.6016e-06 | 2.0473e-05 | 3.7183e-06 | 9.5938e-06 | 9.7352e-07 | 1.2107e-08 | 3.1769e-07 | 1.3128e-13 | 2.8457e-06 | 5.3517e-06 | 1.3368e-05 | 9.6359e-08 | 2.2914e-08
EF 3.0 normalized and weighted